Quality Assurance Program Plan

for

Environmentally Concerned Citizens of South Central Michigan

(ECCSCM)

Water Monitoring Project

August, 2002

Table of Contents

I.  Project Description

II.  Project Organization and Responsibilities

III.  Data Management, Analysis, and Reporting Plans

I.  Project Description

The ECCSCM Water Monitoring Project, funded by a Community Action Grant from Sierra Club, conducts surface water monitoring for E. coli bacteria and Dissolved Oxygen at sites near Confined Animal Feed Operations in the Hudson, Michigan, area (Lenawee and Hillsdale Counties).  Several sampling sites are in the River Raisin Watershed; most sites are in the Bean/Tiffin/Maumee Watershed.

The purpose of the Project is to identify surface water quality problems and high risk areas, and to educate the public in water quality and watershed issues.  Sampling results are sent to the Michigan Department of Environmental Quality, Region 5 EPA, and the Lenawee and Hillsdale County Health Departments.  Reports are also published in the quarterly ECCSCM newsletter; and total monitoring data is available to the public.

II.  Project Organization and Responsibilities

ECCSCM Water Monitoring Project Coordinators are ECCSCM members Janet Kauffman, resident of Hudson and professor at Eastern Michigan University, and Kathy Melmoth, R.N., resident of Pittsford and nursery-grower/farmer.  Dissolved Oxygen/water temperature results are taken in the field with a YSI 55 DO meter.  E. coli samples, in sterile bottles supplied by the lab, are delivered on ice within 6 hours to D&A Environmental LLC, Jackson, MI – Michigan certified drinking water lab #9920.  Debra Hayes-Wolf (water@daenvironmental.com) coordinates laboratory analysis and quality assurance for laboratory testing.

Project Coordinators:

Janet Kauffman

Kathy Melmoth, R.N.

Quality Assurance/Laboratory Analysis Coordinator:

Debra Hayes-Wolf

D&A Environmental LLC

Jackson, MI 49203

517-783-3883

Project Coordinator Responsibilities:

Janet Kauffman and Kathy Melmoth, as Project Coordinators, are responsible for the overall quality of the monitoring, including adherence to schedules, budgets, data preparation, reports, summaries.  They are also responsible for overseeing all field-related activities, including scheduling, sampling, and transporting E. coli samples for analysis.

Field Responsibilities/Techniques/Quality Assurance:

YSI DO meter will be used for Dissolved Oxygen/water temperature; meter will be calibrated as per YSI instructions.  E. coli samples will be collected as grab samples following clean technique and appropriate QA/QC procedures.  D&A Environmental LLC will be notified 24 hrs. prior to day of sampling, and samples will be delivered to the lab on ice within 6 hours.

Field volunteers will assist with activities related to sampling – completing paperwork, recording observations, and providing general assistance.  Volunteer work will allow citizens to gain knowledge of correct sampling techniques and will familiarize them with the watershed and water quality issues.

Quality Assurance/Laboratory Analysis Responsibilities:

Debra Hayes-Wolf, as QA/Lab Analysis Coordinator, is responsible for laboratory testing for E. coli and all quality assurance/quality control in laboratory testing.

Laboratory Responsibilites/Quality Assurance Quality Control:

All bacteria analysis and data reporting will be conducted by D&A Environmental LLC.  Anaylsis will be performed in accordance with standard methods, under an appropriate quality assurance/quality control plan.

III.  Data Management, Analysis, and Reporting Procedures

All data gathered in the field will be recorded on log sheets—dates and times of sampling, weather and water conditions, DO/water temp readings.  Both Project Coordinators will maintain copies of original log sheets.  E. coli data generated in the laboratory will be added to log sheets and also entered into a total data Excel spreadsheet, listing data by site.  Raw sampling data will be sent to DEQ, EPA Region 5, Hillsdale and Lenawee Co. Health Departments, Lenawee County Drain Commission.  All reports on findings, quarterly data reports, charts, summaries, will be released by Project Coordinators.  Raw, total data will be available as Excel file to the public.